## Slide 1
領先創新·
·超越自我
2019 Synopsys ARC盃電子設計競賽

## Slide 2: iRobot – Robot System for Front-Vehicle Detection to Enhance Driver's Awareness
Tsang-Yung Wu, Wen-Cong Huang, Kai-Wen Yang
2019.08.27
Team: Magical Robot

## Slide 3: Agenda
Introduction
Technology Breakthrough
Results
Conclusion
References
Appendix

## Slide 4: Agenda
Introduction
Technology Breakthrough
Results
Conclusion
References
Appendix

## Slide 5: Motivation – 3A
AIoT
Connect the World
Augmented Reality
Understand the World
ARC IoTdk
Compute the World

## Slide 6: Prospect
Motivation –
3A
How to produce something interesting?
Start
Front-Vehicle Detection
Urban scenes is easier to get, e.g. CityScapes
Think
Smart Movement Robot
Like Amazon robot that move around warehouse smartly
Goal

## Slide 7: System Architecture
Notes: Prototype
  Car with two wheels in the back one 導向輪 in the front
  Car with ARC and self and Arduino on it
  OV7670 is connected with the ARC and resting on the shelf
  Bluetooth and a motor board are connected with the Arduino
LCD screen
More Specific Application Goal
Difference between segmentation and objection detection
Micro robot

## Slide 8: Agenda
Introduction
Technology Breakthrough
Results
Conclusion
References
Appendix
Notes: 1. how performance changes
2. Testing results or training results
3. why demo looks bad (or good)

## Slide 9: Technology Intro
Semantic
Segmentation
Figure referred from https://towardsdatascience.com/semantic-segmentation-popular-architectures-dff0a75f39d0
Notes: 理解場景->語意分割
例子：自駕車

## Slide 10: Technology Breakthrough
The task of classifying each and very pixel in an image into different classes as shown in figure below
Example Use Cases
  Self-Driving Cars
  Robotic Systems
  Damage Detection
Current Implementation
  Traditional feature extraction
  Deep learning
ICNet
Revised ICNet
ResNet
Final Model
Paper result
reproduce
Experiments & Revision
Hardware Constraint ??

## Slide 11: Method
The task of classifying each and very pixel in an image into different classes as shown in figure below
Example Use Cases
  Self-Driving Cars
  Robotic Systems
  Damage Detection
Current Implementation
  Traditional feature extraction
  Deep learning
Revised ICNet
ResNet
Final Model
ICNet

## Slide 12: Method
The task of classifying each and very pixel in an image into different classes as shown in figure below
Example Use Cases
  Self-Driving Cars
  Robotic Systems
  Damage Detection
Current Implementation
  Traditional feature extraction
  Deep learning
ICNet
ResNet
Final Model
Revised ICNet

## Slide 13: Method
The task of classifying each and very pixel in an image into different classes as shown in figure below
Example Use Cases
  Self-Driving Cars
  Robotic Systems
  Damage Detection
Current Implementation
  Traditional feature extraction
  Deep learning
ICNet
Revised ICNet
ResNet
Final
Model
Reshape input image to much smaller size
Shrink the numbers of channel in convolutional layers
Reduce number of class to 2 most important classes
19 classes
2
key classes
Notes: Revised icnet 依舊複雜 有限的memory情況下選擇使用resnet 並對resnet修改使成為

## Slide 14: Model Feature
ICNet
Revised ICNet
ResNet
Final Model
523KB
113KB
28KB
800fps
2054fps
425fps
Paper Result
Mode Size:
7MB
Input image size:
1024 x 2048
mIoU for all classes:
69.5%
Frame:
30fps
Model Size
Frame
Rate

## Slide 15: Model Feature
ICNet
Revised ICNet
ResNet
Final Model
81.6%
72.4%
79.4%
mIoU for Two Key Classes

## Slide 16: Agenda
Introduction
Technology Breakthrough
Results
Conclusion
References
Appendix

## Slide 17: Segmentation Results on GPU
Cityscapes testing image
Segmentation result
Cityscapes testing image
Segmentation result

## Slide 18: Segmentation Results on ARC
Camera result
segmentation result
Simulative scene
Notes:   Considering the data memory requirement, it is still impossible to download ICNet into the ARC board
  Icnet actual size
  Revisement you do to the ICNET
  Later unfeasible reason the revised ICNet model size

## Slide 19: Scene Understanding – How many cars?

## Slide 20: Scene Understanding – Danger Detection

## Slide 21: iRobot & Urban Scene

## Slide 22: Agenda
Introduction
Technology Breakthrough
Results
Conclusion
Appendix
References

## Slide 23: Conclusion
Notes: Model Compression in Edge-Device
Realize Image Segmentation
  Understand scenes
  Self movement

## Slide 24: Agenda
Introduction
Technology Breakthrough
Results
Conclusion
References
Appendix

## Slide 25: References
Zhao, Hengshuang, et al. "Icnet for real-time semantic segmentation on high-resolution images." Proceedings of the European Conference on Computer Vision (ECCV). 2018.
He, Kaiming, et al. "Deep residual learning for image recognition." Proceedings of the IEEE conference on computer vision and pattern recognition. 2016.
Amazon Robotics
OV7670 Datasheet
https://singularityhub.com/2017/02/10/how-robots-helped-create-100000-jobs-at-amazon/

## Slide 26: Agenda
Introduction
Technology Breakthrough
Results
Conclusion
References
Appendix

## Slide 27: Introduction to OV7670
OV7670 is a low-power CMOS image sensor
Low operating voltage for embedded devices
Configurable through Serial Camera Control Bus (SCCB) interface, which is similar to I2C
Supports multiple color formats e.g., RGB565/555, YUB, and YCbCr

## Slide 28: Using OV7670 with ARC IoT Kit
The SCCB protocol is similar to I2C
Initializing SCCB interface using embARC library
▼ Get I2C device ID
▼ Open I2C as master mode

## Slide 29: Using OV7670 with ARC IoT Kit
Write registers through SCCB
▼ Send STOP after I2C write
▼ Write address and data using embARC I2C functions

## Slide 30: Using OV7670 with ARC IoT Kit
Read registers through SCCB
▼ Send STOP after write address and read data
▼ Write address, then read data from the address

## Slide 31: Using OV7670 with ARC IoT Kit
Differences between I2C and SCCB read access
  I2C
  SCCB
▼ Send RESTART after writing address and STOP after data read
▼ Always send STOP after writing address or data read

## Slide 32: Using OV7670 with ARC IoT Kit
Camera initialization process
  OV7670 configurations from the documentation

## Slide 33: Using OV7670 with ARC IoT Kit
Camera initialization process
  Writing configurations to OV7670 for initialization
▲ Using our writeReg() function to write configuration values

## Slide 34: Using OV7670 with ARC IoT Kit
Generating clock for OV7670
  Clock frequency 24M Hz

## Slide 35: Using OV7670 with ARC IoT Kit
Reading camera pixel clock and data
  At each pixel clock (PCLK) edge, we can read in pixel values from GPIO pins
  However, PCLK is too fast for GPIO function calls
    We use macro _arc_aux_read() in embARC to handle PCLK

## Slide 36: Using embarc_mli library
Extract model coefficients
Define integer and fraction bits per layer
Define weight and bias size of each convolution layer
#define CONV1_W_INT (0)
#define CONV1_B_INT (0)
#define CONV1_OUT_INT (4)
const w_type _W L1_conv_wt_buf[CONV1_W_ELEMENTS] = {
L1_WQ(-0.27608082),L1_WQ(0.1392435),L1_WQ(0.24875988),L1_WQ(-0.29018065),\
L1_WQ(0.000143734),L1_WQ(0.024988562),L1_WQ(-0.08530177),L1_WQ(0.16210964),\
#define CONV1_W_FRAQ (FRQ_BITS(CONV1_W_INT, w_type))
#define L1_WQ(val) QMN(w_type, CONV1_W_FRAQ, val)
#define CONV1_W_SHAPE {32,3,3,3}
#define CONV1_W_ELEMENTS (32*3*3*3)
#define CONV1_B_SHAPE {32}
#define CONV1_B_ELEMENTS (32)

## Slide 37: Using embarc_mli library
Define layers' configuration
Construct the model with functions in mli_kernal_api and mli_helpers_api
  mli_krn_conv2d_chw_fx8
  mli_krn_maxpool_chw_fx8
  mli_krn_eltwise_add_fx8
Data preprocessing and model inference
  seg_preprocessing( img, seg_net_input)
  seg_net()
static const mli_conv2d_cfg shared_conv_cfg = {
.stride_height = 1, .stride_width = 1,
.padding_bottom = 1, .padding_top = 1,
.padding_left = 1, .padding_right = 1,
.relu.type = MLI_RELU_GEN
};